## Slide 1: IT694 Computer Networks
Week14_Lec1

## Slide 2: Virtual LANs (VLANs): motivation
Computer
Science
EE
Q: what happens as LAN sizes scale, users change point of attachment?
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy issues

## Slide 3: Virtual LANs (VLANs): motivation
administrative issues:
CS user moves office to EE - physically attached to EE switch, but wants to remain logically attached to CS switch
Computer
Science
EE
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy, efficiency issues
Q: what happens as LAN sizes scale, users change point of attachment?

## Slide 4: Virtual Local Area Network
A switch that allows multiple Local area networks to be defined over a single physical local area network infrastructure giving an appearance of multiple VLANS on single switch

## Slide 5: Port-based VLANs
1
8
2
7
9
16
10
15
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local Area Network (VLAN)
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
… operates as multiple virtual switches
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)

## Slide 6: Port-based VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 7: VLANS spanning multiple switches But how should these two switches be interconnected?
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports

## Slide 8: 802.1Q VLAN frame format
802.1 Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information
(12 bit VLAN ID field, 3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 9: Trunking Vs Inter VLAN Routing
VLAN trunks are used to span VLANs across multiple devices.
Trunks allow the traffic from multiple VLANs to travel over a single link, while keeping the VLAN identification and segmentation intact.
VLANs are used to segment switched Layer 2 networks for a variety of reasons.
But hosts in one VLAN cannot communicate with hosts in another VLAN
Inter-VLAN routing is the process of forwarding network traffic from one VLAN to another VLAN.
A particular kind of inter-VLAN routing, called “Router-on-a-Stick”, uses a trunk from the router to the switch to enable all VLAN to pass to the router.

## Slide 10
R1 GigabitEthernet 0/0/1 interface is connected to the S1 FastEthernet 0/5 port.
The S1 FastEthernet 0/1 port is connected to the S2 FastEthernet 0/1 port.
These are trunk links that are required to forward traffic within and between VLANs.
To route between VLANs, the R1 GigabitEthernet 0/0/1 interface is logically divided into three subinterfaces, as shown in the table. The table also shows the three VLANs
that will be configured on the switches.

## Slide 11: Synthesis: a day in the life of a web request
our journey down the protocol stack is now complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 12: A day in the life: scenario
Airtle network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
DAU network
68.80.2.0/24
browser
web page
arriving mobile client attaches to network …
requests web page: www.google.com
scenario:
Sounds
simple!

## Slide 13: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet de-muxed to IP de-muxed, UDP de-muxed to DHCP

## Slide 14: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 15: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply

## Slide 16: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Airtel network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
de-muxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS

## Slide 17: A day in the life…TCP connection carrying HTTP
DNS
DNS
DNS
Airtel network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)

## Slide 18: A day in the life… HTTP request/reply
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed