## Slide 1: IT694 Computer Networks
Fundamentals-I

## Slide 2: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 3: Packet-switching: store-and-forward
packet transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec

## Slide 4: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Queueing occurs when work arrives faster than it can be serviced:

## Slide 5: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for some period of time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up

## Slide 6: Alternative to packet switching: circuit switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
commonly used in traditional telephone networks

## Slide 7: Circuit switching: FDM and TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
Time Division Multiplexing (TDM)
time divided into slots
each call allocated its own band, can transmit at max rate of that narrow band
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band (only) during its time slot(s)

## Slide 8: Packet switching versus circuit switching
example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
Q: how many users can use this network under circuit-switching and packet switching?
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
N
users
1 Gbps link
…..
circuit-switching: 10 users
Q: how did we get value 0.0004?
A: HW problem (for those with course in probability only)
packet switching: with 35 users, probability > 10 active at same time is less than .0004 *

## Slide 9: Packet switching versus circuit switching
great for “bursty” data – sometimes has data to send, but at other times not
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior with packet-switching?
  “It’s complicated.” We’ll study various techniques that try to make packet switching as “circuit-like” as possible.
Is packet switching a “slam dunk winner”?
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet switching)?