## Slide 1: IT694 Computer Networks
Application Layer-I

## Slide 2: Application layer: overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 3: Application layer: overview
Our goals:
conceptual and implementation aspects of application-layer protocols
  transport-layer service models
  client-server paradigm
examining application-layer protocols and infrastructure
  HTTP
  SMTP
  DNS
  Video streaming systems, CDNs
Programming network applications
  socket API

## Slide 4: Some network apps
social media
Web
text messaging
e-mail
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
P2P file sharing
voice over IP
real-time video conferencing (e.g., Zoom)
Internet search
remote login
…

## Slide 5: Creating a network app
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation

## Slide 6: Client-server paradigm
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
server:
always-on host
permanent IP address
often in data centers, for scaling
clients:
contact, communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
examples: HTTP, FTP

## Slide 7: Processes communicating
process: program running within a host
within same host
  two processes communicate using inter-process communication (defined by OS)
processes in different hosts
  communicate by exchanging messages
client process: process that initiates communication
server process: process that waits to be contacted
clients, servers

## Slide 8: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
  A: no, many processes can be running on same host

## Slide 9: An application-layer protocol defines:
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
open protocols:
defined in RFCs, everyone has access to protocol definition
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Zoom

## Slide 10: What transport service does an app need?
data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
security
encryption, data integrity, …

## Slide 11: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
connection-oriented: setup required between client and server processes
does not provide: timing, minimum throughput guarantee, security
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup.
Q: why bother? Why is there a UDP?

## Slide 12: Transport service requirements: common apps
application
file transfer/download
e-mail
Web documents
real-time audio/video
streaming audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5Kbps-1Mbps
video:10Kbps-5Mbps
same as above
Kbps+
elastic
time sensitive?
no
no
no
yes, 10’s msec
yes, few secs
yes, 10’s msec
yes and no

## Slide 13: Application layer: overview
Principles of network applications
Web and HTTP
E-mail, SMTP, IMAP
The Domain Name System DNS
video streaming and content distribution networks
socket programming with UDP and TCP

## Slide 14: Web and HTTP
First, a quick review…
web page consists of objects, each of which can be stored on different Web servers
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects, each addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 15: HTTP overview
HTTP: hypertext transfer protocol
Web’s application-layer protocol
client/server model:
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
HTTP request
HTTP response
HTTP request
HTTP response
iPhone running
Safari browser
PC running
Firefox browser
server running
Apache Web
server