## Slide 1: IT694 Computer Networks
Week4 – HTTP_I

## Slide 2: What will we learn?
Understand full web request lifecycle
Place HTTP in networking stack
Client–Server architecture

## Slide 3: A lifecyle of URL request
Name to numerical address conversion
Connection Request to SERVER
Response from SERVER
What happens when you type a URL
  DNS → TCP → HTTP → Response
application
transport
network
link
physical

## Slide 4: Web and HTTP
https://developer.mozilla.org/en-US/docs/Web/HTTP/Guides/Overview

## Slide 5: HTTP overview (continued)
HTTP uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 6: HTTP overview
HTTP: hypertext transfer protocol
Web’s application-layer protocol
client/server model:
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
HTTP request
HTTP response
HTTP request
HTTP response
iPhone running
Safari browser
PC running
Firefox browser
server running
Apache Web
server

## Slide 7: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
header
lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Mozilla/5.0 (Macintosh; Intel Mac OS X 10.15; rv:80.0) Gecko/20100101 Firefox/80.0 \r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character
request line (GET, POST,
HEAD commands)
carriage return, line feed at start of line indicates end of header lines
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 8: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~

## Slide 9: Other HTTP request messages
POST method:
web page often includes form input
user input sent from client to server in entity body of HTTP POST request message
GET method (for sending data to server):
include user data in URL field of HTTP GET request message (following a ‘?’):
www.somesite.com/animalsearch?monkeys&banana
HEAD method:
requests headers (only) that would be returned if specified URL were requested with an HTTP GET method.
PUT method:
uploads new file (object) to server
completely replaces file that exists at specified URL with content in entity body of POST HTTP request message

## Slide 10: HTTP response message
status line (protocol
status code status phrase)
header
lines
data, e.g., requested
HTML file
HTTP/1.1 200 OK
Date: Tue, 08 Sep 2020 00:53:20 GMT
Server: Apache/2.4.6 (CentOS) OpenSSL/1.0.2k-fips PHP/7.4.9 mod_perl/2.0.11 Perl/v5.16.3
Last-Modified: Tue, 01 Mar 2016 18:57:50 GMT
ETag: "a5b-52d015789ee9e"
Accept-Ranges: bytes
Content-Length: 2651
Content-Type: text/html; charset=UTF-8
\r\n
data data data data data ...
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 11: HTTP connections: two types
Non-persistent HTTP
TCP connection opened
at most one object sent over TCP connection
TCP connection closed
downloading multiple objects required multiple connections
Persistent HTTP
TCP connection opened to a server
multiple objects can be sent over single TCP connection between client, and that server
TCP connection closed

## Slide 12: Non-persistent HTTP: example
User enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80 “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index

## Slide 13: Non-persistent HTTP: example (cont.)
User enters URL:
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 14: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time (per object):
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
object/file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request file
RTT
file received
time
time
Non-persistent HTTP response time = 2RTT+ file transmission time

## Slide 15: Persistent HTTP (HTTP 1.1)
Non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open multiple parallel TCP connections to fetch referenced objects in parallel
Persistent HTTP (HTTP1.1):
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects (cutting response time in half)

## Slide 16: HTTP response status codes
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (in Location: field)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes: