## Slide 1: IT694 Computer Networks
Week5-Transport layer-I

## Slide 2
Write a simple protocol for client and server for exchanging a single message

## Slide 3
What if the client has multiple messages to send?

## Slide 4
How does the client get to know if earlier message was received at the server?
How does the server get to know if earlier message was received at the server?

## Slide 5: TCP: overview RFCs: 793,1122, 2018, 5681, 7323
cumulative ACKs
pipelining:
    TCP congestion and flow control set window size
connection-oriented:
  handshaking (exchange of control messages) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
    one sender, one receiver
reliable, in-order byte steam:
    no “message boundaries"
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
Notes: Typical MSS is 1460 bytes

## Slide 6: TCP segment structure
source port #
dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
sequence numbe r
segment seq #: counting bytes of data into bytestream (not segments!)
application
data
(variable length)
data sent by application into TCP socket
A
acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification

## Slide 7: TCP Handshake
First Segment: Client - Sequence number it plans to use (Flags= SYN, SequenceNum= x).
SEcond Segment: Server - 1 segment that both acknowledges the client’s sequence number (Flags= ACK, Ack= x + 1) and states its own beginning sequence number (Flags= SYN, SequenceNum= y).
Third segment: Client - acknowledges the server’s sequence number (Flags= ACK, Ack= y + 1).

## Slide 8: Sequence Numbers and Ack Numbers
The acknowledgment number that Host A puts in its segment is the sequence number of the next byte Host A is expecting from Host B.
The sequence number for a segment is therefore the byte-stream number of the first byte in the segment.

## Slide 9: TCP sequence numbers, ACKs
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: The key thing to note here is that the ACK number (43) on the B-to-A segment is one more than the sequence number (42) on the A-to-B segment that triggered that ACK
Similarly, the ACK number (80) on the last A-to-B segment is one more than the sequence number (79) on the B-to-A segment that triggered that ACK

## Slide 10: Flow Control
Receiver controls flow by telling sender size of currently available buffer measured in bytes
  Window advertisement
Each segment, including data segments, specifies size of window beyond acknowledged byte
  Window size may be zero
    receiver cannot accept additional data at present
    Receiver can send additional acknowledgement later
      buffer space becomes available

## Slide 11: (RDT) stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 12: Performance of (RDT)(stop-and-wait)
example: 1 Gbps link, 15 ms prop. delay, 8000 bit packet
  U sender: utilization – fraction of time sender busy sending
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs
  time to transmit packet into channel:
Notes: if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link
network protocol limits use of physical resources
Let’s develop a formula for utilization

## Slide 13: (RDT) pipelined protocols operation
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged packets
  range of sequence numbers must be increased
  buffering at sender and/or receiver

## Slide 14: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!
Notes: two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 15: Reliable data transfer (RDT) in ACTION
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 16: Reliable data transfer (RDT) in ACTION
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
ack1
send ack1
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
pkt1
(ignore)
rcv ack1

## Slide 17
An institution has a T1 access line (1.544 Mbps) which services web requests
from about 150 users in the network. The institution is considering putting up a proxy server which
can act as a cache for all these users. (I.e., whenever a user makes a web request, the request is first
sent to the proxy server to see if it can service the request from its cache. Otherwise, the proxy
forwards the requests to the origin server.)
a) The users make on the average 1 request per second, with an average size of
a request object being 10 kbits. What percentage of the bandwidth is consumed by the web traffic
when there is no proxy server, and all requests are serviced by the origin server?
b) After installing the proxy server, it was found that the hit rate to the cache is
40%. What percentage of the institutional bandwidth is now consumed by the Web traffic?