## Slide 1: IT694 Computer Networks
IP Addressing

## Slide 2: IP addressing: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 3: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 5: Hierarchical Addressing
Addressing in the Indian mail sys
  Zip code: 382007
  Street: Indroda circle
  Building on street: DAIICT
  Room in building: 21**
  Name of occupant: ABC
Forwarding the mail
  Deliver letter to the post office in the zip code
  Assign letter to mailman covering the street
  Drop letter into mailbox for the building/room
  Give letter to the appropriate person
Divided into network & host portions (left and right)
12.34.158.0/24 is a 24-bit prefix with 28 addresses

## Slide 6: IP Address and a 24-bit Subnet Mask

## Slide 7: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks
  Class B: 10*
    Large /16 blocks
  Class C: 110*
    Small /24 blocks
  Class D: 1110*
    Multicast groups
  Class E: 11110*
    Reserved for future use

## Slide 8: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
  detach each interface from its host or router, creating “islands” of isolated network
  each isolated network is called a subnet
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits